## Slide 1
REVIEW OF COMPUTER NETWORKS
PERTEMUAN 2
IR. NIZIRWAN ANWAR, MT
PROGRAM STUDI TEKNIK INFORMATIKA
FAKULTAS ILMU KOMPUTER

## Slide 2: Computer Network
An interconnected collection of autonomous computers that are capable of exchanging information among themselves.
Components
  Hosts (nodes, end systems)
  Switches
  Communication link

## Slide 3: Internet (Network of networks)

## Slide 4: Types of Networks
According to scale (geographic distribution)
  Wide are network (WAN)
    Distance between any two nodes > 20km and can go as high as thousands of kms
    Long delays due to distance traveled
    Heterogeneity of transmission media
    Speeds of 150Mbps to 10Gbps (OC192 on the backbone)
  Local area network (LAN)
    Limited in geographic scope (usually < 2km)
    Speeds 10-1000 Mbps
    Short delays and low noise
  Metropolitan area network (MAN)
    In between LAN and WAN

## Slide 5: Types of Networks (continued)
Topology
  Irregular
    No regularity in the interconnection – e.g., Internet
  Bus
    Typical in LANs – Ethernet
    Using Carrier Sense Medium Access with Collision Detection (CSMA/CD)
      Listen before and while you transmit
  Star
  Ring
  Mesh

## Slide 6: Topology Network

## Slide 7: Communication Schemes
Point-to-point (unicast)
  One or more (direct or indirect) links between each pair of nodes
  Communication always between two nodes
  Receiver and sender are identified by their addresses included in the message header
  Message may follow one of many links between the sender and receiver using switching or routing
Broadcast (multi-point)
  Messages are transmitted over a shared channel and received by all the nodes
  Each node checks the address and if it not the intended recipient, ignores
  Multi-cast: special case
    Message is sent to a subset of the nodes

## Slide 8: Communication Alternatives
Twisted pair
Coaxial
Fiber optic cable
Satellite
Microwave
Wireless

## Slide 9: Data Communication
Hosts are connected by links, each of which can carry one or more channels
Link: physical entity; channel: logical entity
Digital signal versus analog signal
Capacity – bandwidth
  The amount of information that can be trnsmitted over the channel in a given time unit
Alternative messaging schemes
  Packet switching
    Messages are divided into fixed size packets, each of which is routed from the source to the destination
  Circuit switching
    A dedicated channel is established between the sender and receiver for the duration of the session

## Slide 10: Communication Protocols
Software that ensures error-free, reliable and efficient communication between hosts
Layered architecture – hence protocol stack or protocol suite
TCP/IP is the best-known one
  Used in the Internet

## Slide 11: Protocols TCP/IP vs OSI (compare)

## Slide 12: Message Transmission using TCP/IP

## Slide 13: Classes IP