## Slide 1: Pemrosesan Data Tersebar
Pertemuan 6
The Data Communications Interface Dosen Pengampu: Hendry Gunawan S.Kom, MM
Prodi Teknik Informatika - Fakultas Ilmu Komputer

## Slide 2: Asynchronous and Synchronous Transmission
Timing problems require a mechanism to synchronize the transmitter and receiver
Two solutions
  Asynchronous
  Synchronous

## Slide 3: Asynchronous
Data transmitted on character at a time
  5 to 8 bits
Timing only needs maintaining within each character
Resync with each character

## Slide 4: Asynchronous (diagram)

## Slide 5: Asynchronous - Behavior
In a steady stream, interval between characters is uniform (length of stop element)
In idle state, receiver looks for transition 1 to 0
Then samples next seven intervals (char length)
Then looks for next 1 to 0 for next char
Simple
Cheap
Overhead of 2 or 3 bits per char (~20%)
Good for data with large gaps (keyboard)

## Slide 6: Synchronous - Bit Level
Block of data transmitted without start or stop bits
Clocks must be synchronized
Can use separate clock line
  Good over short distances
  Subject to impairments
Embed clock signal in data
  Manchester encoding
  Carrier frequency (analog)

## Slide 7: Synchronous - Block Level
Need to indicate start and end of block
Use preamble and postamble
  e.g. series of SYN (hex 16) characters
  e.g. block of 11111111 patterns ending in 11111110
More efficient (lower overhead) than async

## Slide 8: Synchronous (diagram)

## Slide 9: Line Configuration
Topology
  Physical arrangement of stations on medium
  Point to point
  Multi point
    Computer and terminals, local area network
Half duplex
  Only one station may transmit at a time
  Requires one data path
Full duplex
  Simultaneous transmission and reception between two stations
  Requires two data paths (or echo canceling)

## Slide 10: Traditional Configurations

## Slide 11: Interfacing
Data processing devices (or data terminal equipment, DTE) do not (usually) include data transmission facilities
Need an interface called data circuit terminating equipment (DCE)
  e.g. modem, NIC
DCE transmits bits on medium
DCE communicates data and control info with DTE
  Done over interchange circuits
  Clear interface standards required

## Slide 12: Characteristics of Interface
Mechanical
  Connection plugs
Electrical
  Voltage, timing, encoding
Functional
  Data, control, timing, grounding
Procedural
  Sequence of events

## Slide 13: V.24/EIA-232-F
ITU-T v.24
Only specifies functional and procedural
  References other standards for electrical and mechanical
EIA-232-F (USA)
  RS-232
  Mechanical ISO 2110
  Electrical v.28
  Functional v.24
  Procedural v.24

## Slide 14: Mechanical Specification

## Slide 15: Electrical Specification
Digital signals
Values interpreted as data or control, depending on circuit
More than -3v is binary 1, more than +3v is binary 0 (NRZ-L)
Signal rate < 20kbps
Distance <15m
For control, more than-3v is off, +3v is on

## Slide 16: Functional Specification
(See table in Stallings chapter 6)

## Slide 17: Local and Remote Loopback

## Slide 18: Procedural Specification
E.g. Asynchronous private line modem
When turned on and ready, modem (DCE) asserts DCE ready
When DTE ready to send data, it asserts Request to Send
  Also inhibits receive mode in half duplex
Modem responds when ready by asserting Clear to send
DTE sends data
When data arrives, local modem asserts Receive Line Signal Detector and delivers data

## Slide 19: Dial Up Operation (1)

## Slide 20: Dial Up Operation (2)

## Slide 21: Dial Up Operation (3)

## Slide 22: Null Modem

## Slide 23: ISDN Physical Interface Diagram

## Slide 24: ISDN Physical Interface
Connection between terminal equipment (c.f. DTE) and network terminating equipment (c.f. DCE)
ISO 8877
Cables terminate in matching connectors with 8 contacts
Transmit/receive carry both data and control

## Slide 25: ISDN Electrical Specification
Balanced transmission
  Carried on two lines, e.g. twisted pair
  Signals as currents down one conductor and up the other
  Differential signaling
  Value depends on direction of voltage
  Tolerates more noise and generates less
  (Unbalanced, e.g. RS-232 uses single signal line and ground)
  Data encoding depends on data rate
  Basic rate 192kbps uses pseudoternary
  Primary rate uses alternative mark inversion (AMI) and B8ZS or HDB3

## Slide 26: Foreground Reading
Stallings chapter 6
Web pages from ITU-T on v. specification
Web pages on ISDN