## Slide 1: SPECTROSCOPY Tools for Structure Determination

## Slide 2
Introduction
  Spectroscopy: the study of the interaction of energy with matter
    Energy applied to matter can be absorbed, emitted, cause a chemical change, or be transmitted
    Spectroscopy can be used to elucidate the structure of a molecule
  Examples of Spectroscopy
    Infrared (IR) Spectroscopy
      Infrared energy causes bonds to stretch and bend
      IR is useful for identifying functional groups in a molecule
    Nuclear Magnetic Resonance (NMR)
      Energy applied in the presence of a strong magnetic field causes absorption by the nuclei of some elements (most importantly, hydrogen and carbon nuclei)
      NMR is used to identify connectivity of atoms in a molecule
    Mass Spectrometry (MS)
      Molecules are converted to ions by one of several methods (including bombardment by a beam of electrons)
      The ions formed may remain intact (as molecular ions, M+), or they may fragment
      The resulting mixture of ions is sorted by mass/charge (m/z) ratio, and detected
      Molecular weight and chemical formula may be derived from the M+ and M+1 ions
      Molecular structure may be deduced from the distribution of fragment ions

## Slide 3
Nuclear Magnetic Resonance (NMR) Spectroscopy
  NMR spectroscopy membantu mengidentifikasi kerangka (framework) carbon-hydrogen dari suatu senyawa organik
  Didasarkan pada penyerapan gelombang radio oleh inti-inti tertentu dalam molekul organik, apabila molekul ini berada dalam medan magnet yang sangat kuat.
  Inti tertentu menunjukkan perilaku seolah-olah mereka berputar (spin), karena inti bermuatan  menciptakan medan magnet

## Slide 4
Contoh Spektra H-NMR  sinyal NMR

## Slide 5: The number of signals
Protons in the same environment are called chemically equivalent protons
Each set of chemically equivalent protons in a compound gives rise to a signal in the 1H-NMR spectrum of that compound

## Slide 6
  Chemical Shift / Pergeseran Kimia : Peak Position in an NMR Spectrum
    Tidak semua inti H membalikkan spinnya tepat sama dengan frekuensi radio  adanya perbedaan lingkungan kimianya dalam molekul
    Posisi dimana muncul sinyal pada spektrum NMR dianamakan chemical shift (pergeseran kimia). Pergeseran kimia merupakan ukuran seberapa jauh sinyal dari sinyal standar TMS
    The most common scale for chemical shifts is the δ (delta) scale. The TMS signal is used to define the zero position on this scale

## Slide 7
Chemical Shift Equivalent and Nonequivalent Protons
    To predict the number of signals to expect in an NMR spectrum it is necessary to determine how many sets of protons are in unique environments
    Chemically equivalent protons are in the same environment and will produce only one signal

## Slide 8
    Example: 1,4-dimethylbenzene
      The spectrum is measured on a delta (d) scale in units of parts per million (ppm)
      Frekuensi terbesar  sebelah kiri spektrum, absorbsinya disebut “medan bawah” (downfield)
      Frekuensi terkecil  sebelah kanan spektrum, absorbsinya disebut “medan atas” (upfield)
      The small signal at d 0 (nol) corresponds to an internal standard (reference) called tetramethylsilane (TMS) used to calibrate the chemical shift scale
      The number of signals in the spectrum corresponds to the number of unique sets of protons
      1,4-dimethylbenzene has protons in two unique environments and so shows two signals

## Slide 9
  Integration of Peak Areas. The Integral Curve
    Area di bawah puncak (luas puncak) berbanding lurus dengan jumlah inti H pada masing-masing lingkungan kimia dalam molekul itu (tinggi puncak proporsional dengan luas puncak)

## Slide 10
  Faktor yang mempengaruhi pergeseran kimia :
    Gugus penarik elektron (elektronegatif) biasanya menyebabkan pergeseran kimia medan bawah
    Keberadaan elektron phi. H yang melekat pada C ik. Majemuk/cincin aromatik muncul di medan bawah dari H pada C jenuh

## Slide 11
        Pergeseran kimia H-NMR

## Slide 13
  Signal Splitting
    Sinyal NMR bisa terjadi pembelahan akibat efek dari medan magnet yang berhubungan dengan proton dari karbon yang berdekatan (bertetangga)
    Characteristic peak patterns result from signal splitting that are related to the number of protons on adjacent carbons
    Signal splitting occurs only when two sets of protons have different chemical shifts (i.e., are not chemical shift equivalent)
    Example: 1,1,2-trichloroethane