## Slide 1
Kuliah 10
Deteksi Protein Bagian II

## Slide 2: Deteksi Protein
BRADFORD
ELISA
Flow Cytometer

## Slide 3: Flow Cytometry Is A Powerful Technique For Characterizing Immune Cells
Allows For Detection Of Surface Markers Of Cells
Allows For Detection Of Intracellular Factors
Allows Detection Of Secreted Factors By Cells
Allows For Detection Of DNA Content

## Slide 4: Principles Of Flow Cytometry

## Slide 5
Fluorescence
Photodiode
Light can be measured at 90° :
Side scatter + Fluorescence
Side scatter reflects the cell content
Laser

## Slide 6
Fluorescence intensity
FITC
FITC
101
104
103
102
Relative fluorescence intensity
Number of Events
FITC
FITC
FITC
FITC
FITC
FITC
FITC
FITC
Notes: 6

## Slide 7: Basics of Flow Cytometry
Cells in suspension
flow in single-file through
an illuminated volume where they
scatter light and emit fluorescence
that is collected, filtered and
converted to digital values
that are stored on a computer
Fluidics
Optics
Electronics

## Slide 8: The automated Microscope
Waste
Detector
& Counter
Sample
This primitive diagram shows the principle: Cells are passing the microscope objective, and an electronic circuit decides whether the cells is fluorescent or not. This is how a flow cytometer works!

## Slide 9: Hydrodynamic focussing in the cuvette
1
Sheath
Sample
Sheath
Sample
Sample pressure low, small core stream. Good for DNA analysis
High sample pressure, broader core stream.
Bad for DNA analysis
LOW
HIGH
Notes: 1

## Slide 10: Limitations With Light Scattering
Some Information Can Be Obtained
FSC Correlates With Cell Size
SSC Correlates With Internal Complexity
To Distinguish Between 2 Cell types
  A. Size Has To Be Different OR
  B. Internal Complexity i.e amount of granules
If These Two Parameters Are The Same, Then No Distinction Can Be Made
See The Following Figure

## Slide 11: FSC vs SSC Dot Plot

## Slide 12: Fluorescence And Antibodies To The Rescue

## Slide 13: Fluorescent Dyes And Antibodies
Fluorochromes Are Molecules That Emit Fluorescence Upon Excitation With Light
  Ex. FITC (Fluorescein Isothiocyanate)
  PE (Phycoerythrin)
  PerCP (Peridinin Chlorophyll Protein)
  APC (Allophycocyanin)
Some Fluorochromes Are Proteins, Some Are Small Organic Compounds
  Ex. PE (Phycoerythrin)-Protein
  Ex. FITC (Fluorescein Isothiocyanate)

## Slide 14: Excitation Spectra Of Fluorochromes

## Slide 15: Emission Spectra

## Slide 16: Architecture of A FacsCalibur Instrument

## Slide 17: Analyzed Data

## Slide 18: Flow Cytometry

## Slide 19: Cell Marker

## Slide 20: Cell Marker

## Slide 21: Fluophore