## Slide 1
Ir. MUH. ARIEF LATAR, MSc
LINGKUNGAN KERJA FAKTOR BIOLOGI

## Slide 2
Bahaya biologi dapat didefinisikan sebagai debu organik yang berasal dari sumber-sumber biologi yang berbeda seperti virus, bakteri, jamur, protein dari binatang atau bahan-bahan dari tumbuhan seperti produk serat alam yang terdegradasi.
BIOLOGICAL HAZARDS

## Slide 3
BAHAYA BIOLOGI/BIOLOGIE HAZARD
NON INFEKSI
organisme viable
racun biogenik
INFEKSI
alergi biogenik

## Slide 4
  IDENTIFIKASI RESIKO BAHAYA BIOLOGI DI TEMPAT KERJA

## Slide 5
  IDENTIFIKASI RESIKO BAHAYA BIOLOGI DI TEMPAT KERJA
  Mikro organisme (bakteri, virus, fungi)  toksin, infeksi, alergi,
  Arthopoda (serangga, dll)  sengatan  infeksi,
  Tumbuhan tingkat tingkat tinggi (toksin & allergen)  dermatitis, asma, pilek,
  Tumbuhan tingkat tingkat rendah (yang membentuk spora),
  Vertebrata (protein allergen)  urine, saliva, faeces, kulit/rambut  allergi,
  Inervertebrata selain Arthopoda (cacing, protozoa)

## Slide 6: BIOLOGICAL HAZARDS
Expos faktor biological -----agents penyebab penyakit
Tipe--- faktor biological –agent/pemuakit
        Bacteria/bakteri
        Viruses/virus
        Fungi/jamur

## Slide 7: HAZARD BIOLOGI
MIKRO ORGANISME (bakteri, virus, fungi)  toksin, infeksi, alergi
ARTHROPODA (serangga, dll)  sengatan  infeksi
TUMBUHAN TINGKAT TINGGI (toksin & allergen)  dermatitis, asma, pilek
TUMBUHAN TINGKAT RENDAH (yang membentuk spora)
VERTEBRATA (protein allergen)  urine, saliva, faeces, kulit/rambut  allergi
INTERVETEBRATA selain ARTHROPODA (cacing, protozoa)

## Slide 8: HAZARD BIOLOGI
POTENSI BAHAYA YANG DISEBABKAN OLEH MAKHLUK HIDUP (BIOLOGI)  GANGGUAN KESEHATAN PADA PEKERJA YANG TERPAJAN
POTENSI BAHAYA YANG MENYEBABKAN RX ALERGI/IRITASI AKIBAT BAHAN-BAHAN BIOLOGIS (debu kapas, dedaunan, bulu, bunga, dll)
TIDAK MEMPUNYAI NILAI AMBANG BATAS (NAB)

## Slide 9: INFEKSI
MASUKNYA KUMAN PATHOGEN KEDALAM TUBUH DAN MENIMBULKAN GANGGUAN KESEHATAN
EXOGENOUS  PENYEBAB INFEKSI DARI LUAR TUBUH
OPORTUNISTIK  KUMAN YANG SEBENARNYA TIDAK GANAS, TAPI KARENA DOSIS BERLEBIH ATAU DAYA TAHAN TUBUH RENDAH
CARRIER  SESEORANG YANG MEMBAWA BIBIT PENYAKIT TANPA MENDERITA SAKIT

## Slide 10: INFEKSI
Masuknya M.O. kedalam tubuh tidak selalu mengakibatkan infeksi, dipengaruhi oleh banyak faktor, al:
  VIRULENSI
  ROUTE OF INFECTION
  DAYA TAHAN TUBUH

## Slide 11: Agent Penyebab Penyakit
VIRUS
HEPATITIS B & HEPATITIS C  menyerang organ hepar/liver/hati, masuk kedalam tubuh melalui:
  Tranfusi darah yang tercemar
  Tertusuk/teriris jarum/pisau yag terkontaminasi
  Hubungan sexual
  Luka jalan lahir waktu melahirkan
  Placenta
  ASI

## Slide 12: Agent Penyebab Penyakit
VIRUS
HUMAN IMMUNODEFISIENCY VIRUS (HIV)  menyebabkan penurunan daya kekebalan tubuh, ditularkan melalui:
    Tranfusi darah yang tercemar
    Tertusuk/teriris jarum/pisau yag terkontaminasi
    Hubungan sexual
    Luka jalan lahir waktu melahirkan
Pekerja berisiko:
    Pekerja RS
    Pekerja yang sering ganti-ganti pasangan

## Slide 13: Agent Penyebab Penyakit
BAKTERI
TUBERKULOSIS  Paru
ANTRHRAX  kulit & paru
BRUCELLOSIS  sakit kepala, artralgia endokarditis
LEPTOSPIROSIS  demam, sakit kepala, mual, gg hati

## Slide 14: Agent Penyebab Penyakit
PARASIT
MALARIA  gigitan nyamuk anopheles
ANXYLOSTOMIOSIS  anemia khronis
JAMUR  gatal-gatal dikulit

## Slide 15: Agent Penyebab Penyakit
HEWAN
SERANGGA  sengatan
BINATANG BERBISA  gigitan  ular
BINATANG BUAS  CARNIVORA

## Slide 16: Agent Penyebab Penyakit
TUMBUHAN
DEBU KAYU  Allergi & asma
DEBU KAPAS  allergi saluran nafas
BINATANG BUAS  CARNIVORA

## Slide 17: JENIS PEKERJAAN YANG BERISIKO
PETUGAS KESEHATAN
PETUGAS PETERNAKAN
PETUGAS PEMBERSIH SELOKAN/SAMPAH
PETUGAS YANG BEKERJA DENGAN KELEMBABAN TINGGI  Jamur kulit (panu, candida, dll)

## Slide 18: TEMPAT KERJA YANG BERISIKO
LAB MIKROBIOLOGI, LAB KESMAS, LAB BIOMOLEKULER
RS & FASILITAS KESEHATAN LAINNYA
FASILITAS BIOTEKNOLOGI
FASILITAS DOKTER HEWAN & BINATANG
PERTANIAN
LAIN-LAIN

## Slide 19: PENGENDALIAN
CONTAINMENT  mencegah pajanan
  Desain tempat kerja
  Peralatan safety (biosafety cabinet, peralatan centrifugal)
  Cara kerja
  Dekontaminasi
  Penanganan limbah dan spill management
BIOSAFETY PROGRAM MANAGEMENT  support dari pimpinan puncak
  Program support, biosafety spesialist, institutional biosafety committee, biosafety manual, OH program, Info & Educt
COMPLIANCE ASSESSMENT
  Audit, annual review, Incident & accident statistics

## Slide 20: PENANGGULANGAN BAHAYA BIOLOGI
MENGENAL BAHAYA-BAHAYA BIOLOGI YANG ADA DI TEMPAT KERJA
MENGHINDARI KONTAK LANGSUNG DENGAN SUMBER PENULAR
MELAKUKAN TINDAKAN ASEPSIS YANG BENAR
MENJAGA KEBERSIHAN DIRI
MENGGUNAKAN ALAT PELINDUNG DIRI YANG SESUAI

## Slide 21: EVALUATION
harmful characteristics of the substance, energy or condition involved
concentration, intensity or level of the exposure to the harmful agent
time duration of the exposure

## Slide 22: CONTROL
elimination
substitution
change of work method
change of work pattern
isolation and segregation
engineering controls
personal protective equipment

## Slide 23: ROUTES OF ATTACK ON THE HUMAN BODY
route of entry : (reach an area of penetration of the body)
process of entry : (penetrate the outer cover of the body)

## Slide 24: ROUTES OF ENTRY
inhalation
ingestion
skin pervasion
injection
implantation
aspiration

## Slide 25: PROCESS OF ENTRY
absorption
      epidermis
      lungs
      gastro-intestinal tract
direct entry into the body

## Slide 26: TOXICOLOGY - the study of poisonous materials and their effects on living organisms
toxic substances
  systemic
    travel through the system
  local
    act only at the point of contact
  cumulative
    not readily excreted from the body
    accumulated over a period of time
toxicity
  LD50 to quantify the effects of a toxic agent
  Acute Toxicity
    harmful effect occurs quickly (seconds, minutes, hours)
  Chronic Toxicity
    harmful effect takes a long time to appear (months, years)

## Slide 27: LOCAL AND SYSTEMIC EFFECTS
local effects (confined to specific area where contact occurs)
  skin
  eye
  respiratory tract
systemic effects (occur at organs distant from contact site)
  liver
  nervous system
  bone
  blood-forming organs

## Slide 28: DEFENCE MECHANISMS OF THE BODY
respiratory defence
  physical filtration
  phagocytosis
lachrymation
immune response
inflammatory response
fibrotic response

## Slide 29: HEALTH EFFECTS CLASSIFICATION OF HAZARDOUS SUBSTANCES
very toxic
toxic
harmful
corrosive
irritant
sensitising
carcinogenic
mutagenic
toxic for reproduction

## Slide 30: APPROVED SUPPLY LIST
general nature of the risk (risk phrase) “causes severe burns”
precautions to be taken (safety phrase) “keep out of reach of children”

## Slide 31: CATEGORIES OF CHEMICAL AGENT
toxic, including carcinogenic
corrosive and irritant
dermatitic and sensitising

## Slide 32: FORMS OF CHEMICAL AGENT
solids
liquids
dusts
fibres
mists
gases
fumes
vapours

## Slide 33: TYPES OF TOXIC EFFECT
respiratory irritants
chemical asphyxiants
haemolytic poisons
narcotics
nervous system poisons
metallic poisons
metallic and polymer fume fever
carcinogens
  halogenated compounds
  nitro-compounds
  aromatic amines
  polycyclic aromatic hydrocarbons
  natural carcinogens
  inorganic carcinogens
  benzene

## Slide 34: TOXIC AGENTS
physical form(s)
mode of entry to body
target organs
symptoms of exposure
  acute
  chronic
occupations at risk

## Slide 35: CORROSIVE AGENTS
destroy living tissue
acids and alkalis
injury through
  contact with skin and eyes
  inhalation
  ingestion

## Slide 36: DERMATITIC AGENTS
primary cutaneous irritants
  contact dermatitis
  at site of contact
  recovery on removal of agent
cutaneous sensitisers
  sensitisation dermatitis
  initial sensitisation
  trace contact enough to cause reoccurrence

## Slide 37: SENSITISERS
respiratory system
  occupational asthma
  inhalation of antigen causes bronchial constriction
sensitisation dermatitis
  isocyanates
  trace contact enough to cause reoccurrence

## Slide 38: OCCUPATIONAL EXPOSURE LIMITS
designed to control the absorption of airborne contaminants into the body
measured in:
    ppm (parts of vapour/gas per million parts of air)
    mg/m3 (milligrams of substance per cubic metre of air)
expressed as the concentration of an airborne substance averaged over a reference period
    15 minutes short term limit
    8 hours long term limit

## Slide 39: OCCUPATIONAL EXPOSURE LIMITS
Maximum Exposure Limit (MEL)
  maximum permissible concentration
  has legal status
  must not be exceeded
  reduce exposure to as far below the MEL as possible
Occupational Exposure Standard (OES)
  concentration at which no evidence of harm
  represents good practice
  if exceeded, take steps to reduce down to OES
  OES represents adequate control

## Slide 40: OCCUPATIONAL EXPOSURE LIMITS
long term limits
  time-weighted average concentration
  conc. x exposure time averaged over 8 hours
  designed to control chronic effects
short term limits
  time-weighted average concentration
  conc. x exposure time averaged over 15 mins
  designed to control acute effects

## Slide 41: CONTROL PHILOSOPHY

## Slide 42
Referensi :
Bird, F.E., Jr., (c.1980)
Mine safety and Loss Control . Loganville, Ga : Intiute Press.
Heinrich, H.W. al al (1980),
Principles of Accident Prevention. Industrial Accident Prevention, New York ; McGraw Hill
Nedved, M etall, (1991)
Fundamentals of Chemical Safety and Major Hazard Control, ILO Publication, genewa
National Safety Counsil (USA),. (1988),
Accident Prevention Manual for Industrial Operations,
Taylor Easter Hegney, (1997),
Enhancing Safety an Auatralian Workplace Primer, Joe Riordan - Chairperson worksafe Auatralia, editor G.A. Taylor cover design Paul rochford, TAFE publication :
Olishifski Julian, McElroy, Frank E. eds.,“Fundamentals of Industrial Hygiene.”, Chicago L Natâ€™l Safety Council
Velle, R. (1980)
Facts About Safety Training . Safery training methods,

## Slide 43: Terima Kasih