## Slide 1: Designing and Implementing a Secure Network Infrastructure
Advanced Network Security

## Slide 2: Technology Fundamentals
Security Policy
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security
How Do You Secure Infrastructure ?

## Slide 3: Security Technology Details
Who cares about technology if you don’t know what you want or need to protect……

## Slide 4: First Step…..Security Policy
What are you trying to protect?
  What data is confidential?
  What resources are precious?
What are you trying to protect against?
  Unauthorized access to confidential data?
  Malicious attacks on network resources?
How do regulatory issues affect your policy?

## Slide 5: Characteristics of a Good Security Policy
Can it be implemented technically?
Are you able to implement it organizationally?
Can you enforce it with security tools and /or sanctions?
Does it clearly define areas of responsibility for the users, administrators, and management?
Is it flexible and adaptable to changing environments?

## Slide 6: Why Should You Care?
Your job may be at stake
Your reputation may be at stake
Why do you not care?
Time for reality check…..most companies STILL DO NOT have corporate sanctioned security policies….operators define them ad-hoc

## Slide 7: Useful Resources
http://www.ietf.org
http://www.sans.org
http://www.microsoft.com/technet/treeview/default.asp?url=/technet/security/default.asp
http://www.robertgraham.com/pubs/network-intrusion-detection.html

## Slide 8: Security Policy Summary
Need to have a comprehensive document for legal support
Need a companion document which all corporate users will actually read

## Slide 9: Cryptography Is Used For ?
Authentication Protocols
Data Origin Authentication
Data Integrity
Data Confidentiality

## Slide 10: Public Key Encryption
Uses public/private keys
  Keep private key private
  Anyone can see public key
Private
Public
Computing Key pair is computationally expensive!!
Common Algorithms: RSA, El Gamal

## Slide 11: Data Origin Authentication
1. Router A generates public/private key pair
2. Router A sends its public key to Router B
3. Router A encrypts packet with its private key and sends encrypted packet to Router B
4. Router B receives encrypted packet and decrypts with Router A’s public key
Pri
Pub
Pub
1
2
3
4
Pri
Pub
Clear
Encrypted
Clear
Router A
Router B
ENCRYPT
DECRYPT

## Slide 12: Secret Key Encryption
Sensitive
Information
Shared Secret Key
Shared Secret Key
Sensitive
Information
(Cleartext)
(Ciphertext)
(Cleartext)
DES
DES
Internet
ENCRYPT
DECRYPT
Common Algorithms: DES, 3DES, AES, IDEA

## Slide 13: Scalability with Secret Key Crypto
Configuring shared secret keys easily becomes administrative nightmare
Automated mechanism to securely derive secret keys => Diffie-Hellman

## Slide 14: Deriving Secret Keys Using Public Key Technology (e.g., Diffie-Hellman)
YA = (aXA) mod p
YB= (aXB) mod p
Z = (YB ) XAmod p
Z = (YA )XB mod p
DES
XA
XB
a , p
By exchanging numbers in the clear, two entities can determine a new unique number (Z), known only to them

## Slide 15: DH Man-in-the-Middle Attack
Diffie-Hellman is subject to a man-in-the-middle attack
Digital signatures of the ‘public values’ can enable each party to verify that the other party actually generated the value
=> DH exchanges need to be authenticated!!
XA
XB
a , p
YA
YB

## Slide 16: Hash Functions
A hash function takes an input message
of arbitrary length and outputs fixed-length
code. The fixed-length output is called the
hash, or the message digest, of the original
input message.
Common Algorithms: MD-5 (128), SHA-1 (160)

## Slide 17: Exclusive –OR Function (X-OR)
1 xor 1 = 0 0 xor 0 = 0
1 xor 0 = 1 0 xor 1 = 1
0 1 1 0 0 1 0 1 xor’ed with 1 1 0 1 0 0 1 1 produces 1 0 1 1 0 1 1 0
1 0 1 1 0 1 1 0 xor’ed with 1 1 0 1 0 0 1 1 produces 0 1 1 0 0 1 0 1

## Slide 18: Computing a Keyed-MAC
Message broken down into n blocks of 512-bits
Shared secret key is xor’ed with specified array to produce K1
Shared secret key is xor’ed a 2nd time with another specified array to produce K2
Hash1 = (1st block of message + K1)MD5
Hash2 = (hash1 + K2)MD5
Hash3 = (2nd block of message + hash2)MD5
Hash(n+1) = (nth block of message + hashn)MD5
HMAC-MD5-96 / HMAC-SHA-96 -> last hash truncated to 96 bits!!

## Slide 19: Digital Signatures
A digital signature is a message appended to a packet
Used to prove the identity of the sender and the integrity of the packet
Routing
Update

## Slide 20: Digital Signatures
Two common public-key digital signature techniques:
    RSA (Rivest, Shamir, Adelman)
    DSS (Digital Signature Standard)
A sender uses its private key to sign a packet. The receiver of the packet uses the sender’s public key to verify the signature.
Successful verification assures:
    The packet has not been altered
    The identity of the sender

## Slide 21: Crypto 101 Summary
Public Key Encryption
  Typically used for data origin authentication
  Often combined with hash function
Secret Key Encryption
  Typically used for data confidentiality
Diffie-Hellman Algorithm
  Uses public-key cryptography to derive secret key
  Exchanges need to be authenticated
Hash Functions
  Easy to compute
  Typically used for data origin authentication and data integrity
Digital Signatures
  Combines hash functions with public key cryptography

## Slide 22: Technology Fundamentals
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security

## Slide 23: Methods of Authentication
Weak
Strong
No username/password
Static username/password
Aging username/password
One-Time Password (OTP)
  S/Key—OTP for terminal login
  PAP—OTP for PPP
Token cards/soft tokens (OTP)
  Enigma Logic, DES Card, Security Dynamics
WHO are you? What credentials do you give?

## Slide 24: One Time Passwords
S/KEY
  List of one-time passwords
Token cards
  Use algorithm based on PIN or time-of-day to generate passwords
  Server uses same algorithm
34 HUM FISH BIRD DIG SCRAP
35 SAVE DUNK FRED SELF HURT
36 RAKE GET HIS BUNK OFF
37 DEAD RUN JACK HIDE LOAD

## Slide 25: Initial S/Key Exchange
Client
Network
Access Server
S/Key Server
PSTN
Initialized with
password “letmein”
Initialized with
password “letmein”
S/Key initialization packet
Reply (seed=6 , sequence num = 98)

## Slide 26: S/Key Password Computation
Client
Network
Access Server
S/Key Server
PSTN
“letmein” + 6
1
98 times
Hash
Function
Hash
Function
2
6-word output
( HARD BITE LOAD HURT SAVE DEAD )
3

## Slide 27: Verifying The S/Key Password
Client
Network
Access Server
S/Key
Server
PSTN
( HARD BITE LOAD HURT SAVE DEAD )
Seq # Password
99 BOAT HIDE LOVE HOME HELP WHAT
( HARD BITE LOAD HURT SAVE DEAD )
Hash
Function
( BOAT HIDE LOVE HOME HELP WHAT )

## Slide 28: S/Key Resources
Free UNIX implementations
Microsoft ?

## Slide 29: Why Is PPP Important?
Multiplex multiple protocols over a single connection
Handle compression and encryption at lowest possible layer
Easy authentication at other end of connection
You use it for dial-up connections

## Slide 30: Do You Use PPPoE?
Encapsulates PPP packets over Ethernet
Simple bridge access device can provide subnet connection to remote access server
Useful in ADSL environments to provide access control, billing and type of service per-user, rather than per-site, basis

## Slide 31: PPP Authentication
PAP
CHAP
MS-CHAP
MS-CHAPv2
EAP
Link establishment (LCP) can be followed by optional authentication phase before proceeding to network layer protocol (NCP) phase.
Client
Network
Access Server
PSTN

## Slide 32: PPP PAP Authentication
Network
Access Server
“Twiggy”
Branch Router
ID Password
Twiggy LetMeIn
DATABASE
Authentication Request
(ID=Twiggy, Password=LetMeIn)
Authenticate-ACK
Compare ID
and password
2
3
1
authenticates only client, authentication only performed once during
session, passwords are sent in the clear ………

## Slide 33: PPP CHAP Authentication
Client and server need to exchange pre-shared secret
Shared secret is used as input to hash function which computed ‘challenge’
Uses repeated challenges whose frequency is up to the authenticator to limit the time of exposure to any single attack
Either CHAP peer can act as authenticator

## Slide 34: PPP CHAP Authentication
“Loopy” NAS
“Twiggy”
Branch Router
Name Secret
Twiggy LetMeIn
DATABASE
Challenge Message
(ID, challenge#, Twiggy)
Challenge Response
Compute and compare
hash values
2
3
1
Name Secret
Loopy LetMeIn
DATABASE
(ID, challenge response # [hash], Loopy)
Compute
hash value
4
5
Success Message

## Slide 35: PPP MS-CHAP /MS-CHAP2
RFC 1994 claims that CHAP secrets cannot be stored in encrypted form
Microsoft has a variation of CHAP where the secrets are stored encrypted by both the peer and the authenticator

## Slide 36: PPP EAP Authentication
Supports multiple authentication mechanisms
Authentication mechanism selected in authentication phase
Permits use of a ‘back-end’ server
NAS can become pass-through and doesn’t need to be updated for new authentication mechanism support

## Slide 37: PPP EAP Authentication
Telecommuter
NAS
EAP server
EAP-Request (Type=Identity)
EAP-Response (Type=Identity with ID info)
Forwarded to Telecommuter
EAP-Response (Type=OTP with OTP info)
Forwarded to Telecommuter
Forwarded to EAP server
EAP-Request (Type=OTP with challenge)
Forwarded to EAP server
EAP-Success (Type=None)

## Slide 38: PPP Authentication Summary
PPP PAP – password sent in clear; no playback protection….PAP should be avoided
PPP CHAP – encrypted password but the password must be stored as cleartext on the server (not with MS-CHAP)
PPP MS-CHAP - proprietary
PPP EAP – most flexible

## Slide 39: Scalable Authentication
AAA: Provides for authentication as well as authorization and accounting
  TACACS+
  RADIUS
Kerberos

## Slide 40: TACACS+ Transactions
Transactions between client and server are authenticated through use of shared secret
Transactions are encrypted
Hash1 = (session ID, secret, version#, seq#) MD5
Hash2 = (hash1, session ID, version#, seq#) MD5
[repeated an implementation specific # of times)
Last hash concatenated and truncated to length of data
to be encrypted….this is called the pseudo-pad
Ciphertext = bytewise XOR on pseudopad with data
to be encrypted
1
2
3

## Slide 41: TACACS+ Header
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Major
Minor
Type
Sequence Number
Flags
Session ID
Length
Major version: major TACAS+ version number
Minor version: minor TACACS+ version number which allows revisions
To the TACACS+ protocol while maintaining backwards compatibility
Type: 0x01=authentication; 0x02=authorization; 0x03=accounting
Seq_num: the first TACACS+ packet in a session must start with 1
And each subsequent packet increments the sequence number by 1
Flags: specifies whether encryption or multiplexing is used
Session ID: randomly chosen and does not change for the duration
Of the TACACS+ session
Length: total length of the TACACS+ packet excluding the header

## Slide 42: A TACACS+ Exchange
PSTN
User
NAS
(TACACS+ client)
TACACS+ Server
User initiates PPP authentication to NAS
NAS sends START packet to TACACS+ server
TACACS+ server responds with GETUSER packets that
contain the prompts for username/password (PAP) or challenge (CHAP)
4. NAS sends the display to the user
5. User responds to NAS
6. NAS sends encrypted packet to TACACS+ server
7. TACACS+ server responds to NAS with authentication result
8. NAS and TACACS+ server exchange authorization requests and replies
9. NAS acts upon authorization exchange
1
2
3
4
5
6
7
8
9
TACACS+ client and server are
pre-configured with a shared key
2
Corporate Net

## Slide 43: RADIUS Transactions
Transactions between client and server are authenticated using shared secret
Only user passwords are encrypted between client and server
Hash1 = (random#, secret) MD5
User password is padded with nulls to get 16-bytes
Encrypted Password = hash1 XOR padded password
1
2
3

## Slide 44: RADIUS Packet Format
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Code
Identifier
Length
Request Authenticator
Attributes
Code: one octet and identifies the type of RADIUS packet
Identifier: one octet and aids in identifying requests and replies
Length: two octets and indicates length of the packet including the
Code, Identifier, Length, Authenticator and Attribute fields. The minimum
Length is 20 and the maximum is 4096 octets.
Authenticator: 16 octets whose value is used to authenticate the reply
From a RADIUS server and is used in the password encryption algorithm
Attributes: specifies what RADIUS services are used

## Slide 45: RADIUS Login and Authentication
User initiates PPP authentication to NAS
NAS prompts user for username/password (PAP) or challenge (CHAP)
User replies
4. NAS sends username and encrypted password to RADIUS server
5. RADIUS server responds with Accept, Reject or Challenge
6. NAS acts upon services and service parameters bundled with Accept or Reject
PSTN
Corporate Net
User
NAS
(RADIUS client)
RADIUS Server
1
2
3
4
5
6
RADIUS client and server are
pre-configured with a shared key
2

## Slide 46: TACACS+ vs RADIUS
TACACS+: TCP port 49
RADIUS: UDP port 1812 (1645)
Only password is confidential in RADIUS
Feature support
Vendor support
PSTN
Corporate Net
NAS
(RADIUS client)
RADIUS / TACACS+
server
Where is info sent in cleartext?!?

## Slide 47: Keberos
Designed at MIT
Uses DES for encryption and authentication
Uses a trusted third party (the KDC) to issue ‘tickets’ to users

## Slide 48: Kerberos Keys
Kclient
Kserver
Client
KDC
Application
Server
Shared key between
KDC and client
Shared key between
KDC and application server

## Slide 49: Kerberos Authentication Request and Reply
Client
KDC
Principals with
associated keys
and access rights
DATABASE
Authentication Request
Authentication Response
[Ksession, Texp, random #, server name] encrypted with Kclient
[Kerberos Ticket] encrypt with Kserver
Client prompts user for password and uses the
password, Kclient, to decrypt the session key Ksession
4
3
2
1
KDC verifies client
access rights

## Slide 50: Kerberos Application Request and Reply
Client
KDC
[Kerberos Ticket] encrypted with Kserver
Application Response
[Authenticator] encrypted with Ksession
Application Request
Server decrypts Kerberos ticket to get
session key. This session key is used
to decrypt the authenticator.
[Authenticator] encrypted with Ksession
(used if mutual authentication required)
1
2
3

## Slide 51: Kerberos Timestamps
Since Kerberos has a time-dependency issue through use of timestamps, a synchronized dependable mechanism of obtaining time is needed.

## Slide 52: Adding Access Control
Wouldn’t it be cool if access to network points was denied unless successfully authenticated?
That’s what 802.1x standard
can be used for……

## Slide 53: IEEE 802.1x
Supplicant
Authenticator
Authentication
Server
IEEE specification that enables authentication and key
management for IEEE 802 local area networks
Utilizes EAP for authentication

## Slide 54: 802.1x Transaction Example
Supplicant
Authenticator
Authentication
Server
Workstation
LAN Switch
RADIUS Server
EAP over EAPOL
EAP over RADIUS
When supplicant physically connects the
switch port enables port only for EAPOL traffic
Initial EAP packet exchange using EAPOL
Switch translates between EAP EAPOL messages and EAP RADIUS
messages and acts as pass-thru between workstation and server
If EAP is successful the RADIUS server can optionally send
further authorization information to the switch
1
2
3
4

## Slide 55: Authentication Technology Summary
Try to use one-time passwords wherever possible.
PPP EAP with RADIUS is very flexible and scalable solution for dial-in environments.
AAA solutions can be used in conjunction with most authentication functionality and give added benefit of authorization and accounting.
802.1x will replace proprietary port authentication features.

## Slide 56: Technology Fundamentals
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security

## Slide 57: Application Layer Security
S-HTTP: allows request and reply messages to be signed, authenticated, encrypted, or any combination of these (including no protection).
S/MIME: for email and messaging protocols

## Slide 58: S/MIME Security Services
Authentication
Message integrity and nonrepudiation of origin (using digital signatures)
Privacy and data security (using symmetric encryption)
It is up to implementation to decide
whether to sign or encrypt first !!

## Slide 59: Technology Fundamentals
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security

## Slide 60: Transport Layer Security (SSL/TLS)
Provides data encryption, server authentication, message integrity, and optional client authentication for a TCP/IP connection.
3 Main Properties:
The connection is private. Encryption is used after an initial handshake to define a secret key. Symmetric cryptography is used for data encryption (for example, DES and RC4).
The peer’s identity can be authenticated using asymmetric, or public key, cryptography (for example, RSA and DSS).
The connection is reliable. Message transport includes a message integrity check using a keyed MAC. Secure hash functions (such as SHA and MD5) are used for MAC computations.

## Slide 61: SSL/TLS Record Format
DATA
HMAC-MD5
Padding
Padding
Length
8 bytes
Type
Version
Length

## Slide 62: The SSL Handshake Process
Internet
SSL Client
SSL Server
Client initiates SSL connection / sends supported cipher suites
Server returns digital certificate to client and selected cipher suite
Client sends encrypted shared secret
Message encryption and integrity algorithms are negotiated
Secure session tunnel is established
Session keys are generated
1
6
5
4
3
2

## Slide 63: SSL Client Authentication
Client authentication (certificate based) is optional and not often used
Many application protocols incorporate their own client authentication mechanism such as username/password or S/Key
These authentication mechanisms are more secure when run over SSL

## Slide 64: SSL/TLS IANA Assigned Port Numbers
Protocol | Defined Port Number | SSL/TLS Port Number
HTTP | 80 | 443
NNTP | 119 | 563
SMTP | 110 | 995
FTP-Data | 20 | 989
FTP-Control | 21 | 990
Telnet | 23 | 992

## Slide 65: Secure Shell (SSH)
Secure low-level transport protocol
Provides strong encryption, cryptographic host authentication, and integrity protection
Authentication is host-based and does not perform user authentication
A higher-level protocol for user authentication can be designed on top of SSH.
The key exchange method, the public key algorithm, the symmetric encryption algorithm, the message authentication algorithm, and the hash algorithm are all negotiated.
Widely supported across multiple operating systems.

## Slide 66: Technology Fundamentals
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security

## Slide 67: IPsec
Suite of protocols to secure IP traffic
  Defined in RFC 2401-2409, RFC 2451
  Ietf.org/html.charters/ipsec-charter.html

## Slide 68: What Does IPsec Provide?
Confidentiality….many algorithms to choose from
Data integrity and source authentication
  Data “signed” by sender and “signature” verified by the recipient
  Modification of data can be detected by signature “verification”
  Because “signature” based on a shared secret, it gives source authentication

## Slide 69: What Does IPsec Provide?
Anti-replay protection
  Optional : the sender must provide it but the recipient may ignore
Key Management
  IKE – session negotiation and establishment
  Sessions are rekeyed or deleted automatically
  Secret keys are securely established and authenticated
  Remote peer is authenticated through varying options

## Slide 70: What is an SA?
Security Association groups elements of a conversation together
  AH authentication algorithm and keys
  ESP encryption algorithm and key(s)
  Cryptographic syncronization
  SA lifetime
  SA source address
  Mode (transport or tunnel)

## Slide 71: A Security Association Maps:
From a host or gateway
  To a particular IP destination address
  With a particular security protocol (AH/ESP)
  Using SPI selected by remote host or gateway
To a host or gateway
  To (one of) our IP address(es)
  With a particular security protocol (ESP/AH)
  Using SPI selected by us

## Slide 72: A SPI Represents an SA
The SPI is a 32-bit number
The SPI is combined with the protocol (AH/ESP) and destination IP address to uniquely identify an SA
An SA is unidirectional
When an ESP/AH packet is received, the SPI is used to look up all of the crypto parameters

## Slide 73: IPsec Traffic Selectors
Selectors for traffic matches….what kind of traffic will be acted on how
Selectors include:
  IP address or range
  Optional IP protocol (UDP, TCP, etc)
  Optional layer 4 (UDP, TCP) port
Selected traffic is either protected with IPsec or dropped

## Slide 74: IPsec Components
AH
  RFC requires HMAC-MD5-96 and HMAC-SHA1-96….older implementations also support keyed MD5
ESP
  RFC requires DES 56-bit CBC and Triple DES. Can also use RC5, IDEA, Blowfish, CAST, RC4, NULL
IKE

## Slide 75: Authentication Header (AH)
Authentication is applied to the entire packet, with the mutable fields in the IP header zeroed out
If both ESP and AH are applied to a packet, AH follows ESP

## Slide 76: AH Header Format
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Next Header
Payload Length
Reserved
Security Parameter Index (SPI)
Sequence Number
Next Header: which higher level protocol is (UDP,TCP,ESP) next
Payload Length: size of AH in 32-bit longwords, minus 2
Reserved: must be zero
SPI: arbitrary 32-bit number that specifies to the receiving device which security
association is being used (security protocols, algorithms, keys, times, addresses, etc)
Sequence Number: start at 1 and must never repeat. It is always set but receiver
may choose to ignore this field
Authentication Data: ICV is a digital signature ov er the packet and it varies in length
depending on the algorithm used (SHA-1, MD5)
Authentication Data
[ Integrity Value Check (ICV) ]

## Slide 77: Encapsulating Security Payload (ESP)
Must encrypt and/or authenticate in each packet
Encryption occurs before authentication
Authentication is applied to data in the IPsec header as well as the data contained as payload

## Slide 78: ESP Header Format
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Next Header
Padding Length
SPI: arbitrary 32-bit number that specifies SA to the receiving device
Seq #: start at 1 and must never repeat; receiver may choose to ignore
IV: used to initialize CBC mode of an encryption algorithm
Payload Data: encrypted IP header, TCP or UDP header and data
Padding: used for encryption algorithms which operate in CBC mode
Padding Length: number of bytes added to the data stream (may be 0)
Next Header: the type of protocol from the original header which appears in the encrypted part of the packet
Authentication Header: ICV is a digital signature over the packet and it varies in length depending on the algorithm used (SHA-1, MD5)
Payload Data (Variable)
Padding (0-255 bytes)
Initialization Vector (IV)
Sequence Number
Security Parameter Index (SPI)
Authentication Data (ICV)
ENCRYPTED

## Slide 79: Packet Format Alteration for AH Transport Mode
Original
IP Header
TCP/UDP
Data
Original
IP Header
AH
Header
TCP/UDP
Data
Authentication Header
Before applying
AH:
After applying
AH:
Authenticated except for
mutable fields in IP header
ToS
TTL
Header Checksum
Offset
Flags

## Slide 80: Packet Format Alteration for ESP Transport Mode
Original
IP Header
TCP/UDP
Data
Original
IP Header
ESP
Header
Encapsulating Security Payload
Before applying
ESP:
After applying
ESP:
Encrypted
ESP
Authentication
Authenticated
TCP/UDP
Data
ESP
Trailer

## Slide 81: Packet Format Alteration for AH Tunnel Mode
Original
IP Header
TCP/UDP
Data
New
IP Header
AH
Header
Data
Authentication Header
Before applying
AH:
After applying
AH:
Authenticated except for
mutable fields in new IP header
Original
IP Header
ToS
TTL
Header Checksum
Offset
Flags

## Slide 82: Packet Format Alteration for ESP Tunnel Mode
Original
IP Header
TCP/UDP
Data
New
IP Header
ESP
Header
Encapsulating Security Payload
Before applying
ESP:
After applying
ESP:
Encrypted
ESP
Authentication
Authenticated
Original
IP Header
TCP/UDP
Data
ESP
Trailer

## Slide 83: Internet Key Exchange (IKE)
Phase I
  Establish a secure channel (ISAKMP/IKE SA)
  Using either main mode or aggressive mode
Phase II
  Establishes a secure channel between computers intended for the transmission of data (IPsec SA)
  Using quick mode

## Slide 84: Overview of IKE
Traffic which needs
to be protected
IPsec Peer
IPsec Peer
IKE Phase 1
Secure communication channel
IKE Phase 2
IPsec Tunnel
Secured traffic exchange
1
2
3
4

## Slide 85: ISAKMP Header Format
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Initiator Cookie
Total Length of Message
Flags
Responder Cookie
Next Payload
Exchange Type
Message ID
Major
Version
Minor
Version

## Slide 86: ISAKMP Message Format
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
Next Payload: 1byte; identifier for next payload in message. If it is the last payload
It will be set to 0
Reserved: 1byte; set to 0
Payload Length: 2 bytes; length of payload (in bytes) including the header
Payload: The actual payload data
Next Payload
Reserved
Payload Length
Payload
Next Payload
Reserved
Payload Length
Payload
ISAKMP HEADER

## Slide 87: IKE Phase 1 Main Mode
Main mode negotiates an ISAKMP SA which will be used to create IPsec Sas
Three steps
  SA negotiation (encryption algorithm, hash algorithm, authentication method, which DF group to use)
  Do a Diffie-Hellman exchange
  Provide authentication information
  Authenticate the peer

## Slide 88: IKE Phase 1 Main Mode
Responder
Initiator
1
2
IKE Message 1 (SA proposal)
IKE Message 2 (accepted SA)
IKE Message 3 (DH public value, nonce)
IKE Message 4 (DH public value, nonce)
IKE Message 5 (Authentication material, ID)
IKE Message 6 (Authentication material, ID)
4
3
Negotiate
IKE Policy
Authenticated
DH Exchange
Compute DH shared secret
and derive keying material
Protect IKE
Peer Identity
Internet
(Encrypted)

## Slide 89: What Is Diffie-Hellman?
First public key algorithm (1976)
Diffie Hellman is a key establishment algorithm
  Two parties in a DF exchange can generate a shared secret
  There can even be N-party DF changes where N peers can all establish the same secret key
Diffie Hellman can be done over an insecure channel
IKE authenticates a Diffie-Hellman exchange 3 different ways
  Pre-shared secret
  Nonce (RSA signature)
  Digital signature

## Slide 90: IKE Phase 1 Aggressive Mode
Uses 3 (vs 6) messages to establish IKE SA
No denial of service protection
Does not have identity protection
Optional exchange and not widely implemented

## Slide 91: IKE Phase 2 Quick Mode
All traffic is encrypted using the ISAKMP/IKE Security Association
Each quick mode negotiation results in two IPsec Security Associations (one inbound, one outbound)
Creates/refreshes keys

## Slide 92: IKE Phase 2 Quick Mode
Responder
Initiator
3
Compute keying material
Internet
Message 1 (authentication/keying material and SA proposal)
Message 2 (authentication/keying material and accepted SA)
Message 3 (hash for proof of integrity/authentication)
1
2
5
Validate
message 1
7
4
6
Validate
message 3
Validate
message 2

## Slide 93: IKE Summary
Negotiates parameters to establish and secure a channel between two peers
Provides mutual authentication
Establishes authenticated keys between peers
Manages IPsec SAs
Provides options for negotiation and SA establishment
LOOK FOR IKE v2 !!!

## Slide 94: IPsec Issues
Dynamic Addressing
NAT/PAT
Device vs User Authentication

## Slide 95: NAT/PAT Problems
NAT/PAT
Router
Remote
Router
Corporate
Network
Branch Network
192.168.1.20
192.168.1.15
144.254.9.30
Original
SRC IP
Translated
SRC IP
Original
SRC Port
Translated
SRC Port
Original
DST IP
Original
DST Port
192.168.1.20
192.150.6.65
144.254.9.30
192.168.1.15
192.150.6.65
144.254.9.30
80
80
2654
6789
5876
6788
Private src IP address converted to globally unique address
(192.168.1.20 -> 192.150.6.65)
Reply to IP address 192.150.6.65
dst IP address translated to private
IP address using port numbers to
help with demultiplexing
(192.150.6.65 -> 192.168.1.20)

## Slide 96: UDP Encapsulation of Transport Mode ESP Packets
Original
IP Header
TCP/UDP
Data
Transport Mode
After applying
ESP/UDP:
Original
IP Header
ESP
Header
Encrypted
ESP
Authentication
Authenticated
TCP/UDP
Data
ESP
Trailer
UDP
Header

## Slide 97: UDP Encapsulation of Tunnel Mode ESP Packets
Original
IP Header
TCP/UDP
Data
Tunnel Mode
After applying
ESP/UDP:
New
IP Header
ESP
Header
Encrypted
ESP
Authentication
Authenticated
Original
IP Header
TCP/UDP
Data
ESP
Trailer
UDP
Header

## Slide 98: Technology Fundamentals
Crypto 101
Authentication Technologies
Application Layer Security
Transport Layer Security
Network Layer Security (IPsec)
Link Layer Security

## Slide 99: Dial-Up VPNs
Treat remote dial access as virtual (Point-to-point) links
  Primary goal of L2 VPNs is tunneling, not security
  Traditional dial-up user authentication (PAP, CHAP, MS-CHAP, EAP)
  In some cases, data confidentiality

## Slide 100: Layer 2 Tunneling Protocol
Designed in IETF PPP Extensions working group
  Combination of Cisco L2F & PPTP features, L2TP RFC 2661, Aug 99
  L2TP Extensions working group established
Uses UDP for control and data packets, well known port is 1701
Uses PPP for packet encapsulation – carries most protocols (also non-IP protocols)
IP UDP packet security provided by IPsec transport mode, as in RFC 2401, 2409, etc

## Slide 101: L2TP Features
Control session authentication, keep-alives
EAP…broader authentication mechanisms
Tunnel over any switched virtual connection (IP, FR, ATM)….runs over any transport
Integration with mobile IP
IPsec ESP for confidentiality and integrity (else packets in the ‘clear’)
IKE for key management

## Slide 102: L2TP and IPsec
TCP
UDP
Application Data
UDP
IP
IP
IPSEC
L2TP
PPP
IPSEC
IPsec DES or 3DES encrypted
Multiple Encapsulations
…..careful of packet size!!
Ping with large MTU size….help discover fragmentation issues!!

## Slide 103: MPLS VPNs
Any VPN is not automagically secure. You need to add security functionality to create secure VPNs. That means using firewalls for access control and probably IPsec for confidentiality and data origin authentication.

## Slide 104: Security……
Vast quantities of security technologies
The challenge — enable you as an ISP to implement a single policy
Get vendors to simplify configurations (what are reasonable defaults?!?)
Need to identify threats and vulnerabilities
Not Just a Technology Problem

## Slide 105: Definitions
Threat: any person, object, or event that, if realized, can potentially cause damage to the network or networked device.
Vulnerability: a weakness in a network that can be exploited by a threat.

## Slide 106: Types of Network Threats
Unauthorized Access
  Eavesdropping/Port scanning/War dialing
Impersonation
  Spoofing attacks/Replay attacks
Data Manipulation
Denial of Service (DoS) / DDoS
Viruses
Email SPAM
Which are you susceptible to ?!?!?

## Slide 107: Example Reconnaissance Attempt
Intruder
1
2
3
DNS query to figure out
which web-servers available
Ping sweep to see which
servers alive and accessible
Port scan to see which
services are available
for exploitation
DNS Servers
Web Servers
Target Host

## Slide 108: War Dialing
1
Intruder finds list
of corporate phone
numbers in phone book
2
War dialing application
Initiated using phone
number block 732-XXXX
3
Answered numbers
are accessible via database
4
5
Intruder attempts to
connect to devices that
answered via deceptive route
Insecure corporate
modem bank allows
unauthorized access
Large Interesting
Corporation
Intruder

## Slide 109: DoS and DDoS Attacks
  TCP SYN
  TCP ACK
  UDP, ICMP, TCP floods
  Fragmented Packets
  IGMP flood
  Spoofed and un-spoofed

## Slide 110: TCP Packet Format
0
4
8
16
31
Destination TCP Port Number
Options (if any)
Padding
DATA................
Source TCP Port Number
Sequence Number
Acknowledgment Number
Offset
Reserved
Window Size
TCP Checksum
Urgent Pointer
A
P
R
S
F
U
R
C
S
S
Y
I
G
K
H
T
N
N

## Slide 111: Basics of a DDoS Attack
DDoS
handler
DDoS
handler
DDoS
handler
DDoS
agents
Victim
DDoS Traffic
DDoS client

## Slide 112: Automated DDoS Attack
1
2
3
4
4
4
5
5
5
Initiate scan
Vulnerable hosts
are compromised
Attack tool installed on
each compromised host
Further scanning
for compromises
Massive DDoS
attack launched
Victim Network
Attacker

## Slide 113: DDoS Vulnerabilities
Distributed and/or coordinated attacks
  Increasing rate and sophistication
Infrastructure protection
  Coordinated attack against infrastructure
  Attacks against multiple infrastructure components
Overwhelming amounts of data
  Huge effort required to analyze
  Lots of uninteresting events

## Slide 114: What If Router Becomes Attack Target?
It allows an attacker to:
Disable the router & network…
Compromise other routers…
Bypass firewalls, IDS systems, etc…
Monitor and record all outgoing an incoming traffic…
Redirect whatever traffic they desire…

## Slide 115: Router CPU Vulnerabilities
CPU Overload
  Attacks on applications on the Internet have affected router CPU performance leading to some BGP instability
  100,000+ hosts infected with most hosts attacking routers with forged-source packets
  Small packet processing is taxing on many routers…even high-end
  Filtering useful but has CPU hit

## Slide 116: Router Security Considerations
Segment areas for route redistribution and ensure limited access to routers in critical backbone areas
Design networks so outages don’t affect entire network but only portions of it
Control router access….watch against internal attacks on these systems. Use different passwords for router enable and monitoring system root access.
Latest scanning craze for http access!!!

## Slide 117: What Is Wrong Here?
Engineering LAN
Corporate Network
House with Computer
Workstation
with Modem
Secure
Engineering Server

## Slide 118: How Do You Secure Infrastructure ?
Securing Infrastructure Devices
Routing Protocol Security
Securing the Network Perimeter (Edge)
Securing Remote Access
Mitigating DDoS Attacks

## Slide 119: Infrastructure Device Integrity
Who has physical access?
Who has logical access?
What is confidential?

## Slide 120: Device Access Security
Physical Location
  Limit physical access to devices
Logical Access
  Console Access
    How is it authenticated?
    How long before timeout?
  Virtual Terminal Access
    How is it authenticated?
    How long before timeout?
    Specify specific hosts?

## Slide 121: Secure Configurations
Secure console and virtual terminal access
  Simple clear-text password (YUK!!)
  TACACS+/RADIUS with clear-text or token card
  SSH
  Kerberos v5
Multiple privilege levels for configuration and user commands
Encrypted passwords when viewing configurations

## Slide 122: Do NOT Even Think of Using Telnet
Telnet is a bad idea!
Avoid it from the start
Telnet sends username and password information across the wire in plain text format.
Do not use telnet to gain access to any of your boxes (router-to-router could be exception for troubleshooting, but limit access in these instances)

## Slide 123: SSH
Two flavors of ssh, ssh1 and ssh2
Use ssh2 if possible
In general the client connecting to your ssh server will either "speak" ssh1 or ssh2
Openssh from http://www.openssh.org/ this can support both
ssh has the advantage that username and password information is sent across the line encrypted and it is non-trivial to break this encryption

## Slide 124: Example – NOT Very Secure
service password-encryption
enable secret 5 $1$mgfc$lSYSLeC6ookRSV7sI1vXR.
enable password 7 075F701C1E0F0C0B
!
username staff password 7 104F0B0A0A1B071F5D547A
line con 0
!
line vty 0 4
exec-timeout 0 0
login local
transport input telnet

## Slide 125: Banner….what’s wrong?
banner login ^C
Martini
2.5 ounces vodka
1/5 ounce dry vermouth
Fill mixing glass with ice, add vermouth and
vodka, and stir to chill. Strain into a Martini
glass and garnish with an olive or lemon twist.
RELAX....INDULGE.....Get Off My Router!!
^C

## Slide 126: Better Device Banner
!!!! WARNING !!!!
You have accessed a restricted device.
All access is being logged and any unauthorized access will be prosecuted to the full extent of the law.

## Slide 127: Device Integrity Checklist
Secure logical access to routers with passwords and timeouts
Restrict logical access to specified trusted hosts
Never leave passwords in clear-text
Shut down unused interfaces
Shut down unneeded services
Test device integrity on a regular basis

## Slide 128: How Do You Secure Infrastructure ?
Securing Infrastructure Devices
Routing Protocol Security
Securing the Network Perimeter
Securing Remote Access
Mitigating DDoS Attacks

## Slide 129: Securing Router-to-Router Communication
Route authentication
Routing filters
Encryption
Routing Updates
144.254.5.101
144.254.5.102
144.254.101.0
144.254.102.0

## Slide 130: Route Authentication
Signature
Signs Route Updates
Route Updates
Verifies Signature
Campus
Certifies authenticity of neighbor and integrity of route updates

## Slide 131: Plaintext Neighbor Authentication
Sending Router
Receiving Router
Campus
Routing Update
Router
Key
SantaCruz
SantaCruz
SanJose
Venice
1
2
3
Routing Update REJECTED

## Slide 132: MD-5 Neighbor Authentication: Originating Router
Hash
Function
Router A
Routing Update
Hash
Routing Update
Hash

## Slide 133: MD-5 Neighbor Authentication: Receiving Router
Hash
Function
Router B
Routing Update
Hash
Routing Update
Hash
Hash
Receiving Router Separates Routing Update and Hash
The Routing Update and the Preconfigured Shared Key are used as Input to the Hash Function
If Hashes Are Equal, Routing Update Is Accepted

## Slide 134: Routing Security Summary
Always turn on MD5 authentication
Always filter routing updates…. especially be careful of redistribution
How paranoid are you?
  Specify which neighbors are allowed to speak to each other

## Slide 135: How Do You Secure Infrastructure ?
Securing Infrastructure Devices
Routing Protocol Security
Securing the Network Perimeter
Securing Remote Access
Mitigating DDoS Attacks

## Slide 136: Role of the Router
Forwards packets at network layer
First point of entry TO a trusted network domain
Last point of exit FROM a trusted network domain
Trusted
Network
Domain
UnTrusted
Network
Domain

## Slide 137: RFC2827 – Ingress Filtering
If an ISP is aggregating routing
announcements for multiple downstream
networks, strict traffic filtering should be
used to prohibit traffic which claims to have
originated from outside of these aggregated
announcements.

## Slide 138: RFC2827 – Ingress Filtering
The ONLY valid source IP address for packets originating from that PC is the one assigned by the ISP (whether statically or dynamically assigned).
The remote access server could check every packet on ingress to ensure the user is not spoofing the source address on the packets which he is originating.

## Slide 139: IP Header Format
0
4
8
16
31
Version
IHL
Type of Service
Total Length (in bytes)
Identification
Flags
Fragmentation Offset
Time to Live
Protocol
Header Checksum
Source IP Address
Destination IP Address
Options (if any)
Padding
DATA................

## Slide 140: TCP Header Format
0
4
8
16
31
Destination TCP Port Number
Options (if any)
Padding
DATA................
Source TCP Port Number
Sequence Number
Acknowledgment Number
Offset
Reserved
Flags
Window Size
TCP Checksum
Urgent Pointer

## Slide 141: UDP Header Format
Source UDP Port
Destination UDP Port
Length
Checksum
Data............
0
16
31

## Slide 142: Filtering Recommendations
Log filter port messages properly
Allow only internal addresses to enter the router from the internal interface
Block packets from outside (untrusted) that are obviously fake or commonly used for attacks
Block packets that claim to have a source address of any internal (trusted) network.

## Slide 143: Filtering Recommendations
Block incoming loopback packets and RFC 1918 networks
  127.0.0.0
  10.0.0.0 – 10.255.255.255
  172.16.0.0 – 172.31.0.0
  192.168.0.0 – 192.168.255.255
Block multicast packets (if NOT using multicast)
Block broadcast packets (careful of DHCP and BOOTP users)
Block incoming packets that claim to have same destination and source address

## Slide 144: Filtering Issues
Ordering
  What sequence is packet inspected in?
Performance
  Are there any limitations?
Logging
  Get appropriate information
  Timestamps

## Slide 145: How Do You Secure Infrastructure?
Securing Infrastructure Devices
Routing Protocol Security
Securing the Network Perimeter
Securing Remote Access
Mitigating DDoS Attacks

## Slide 146: Access VPN
Corporate
Network
VPN
Concentrator
ISP
1
2
3
4
5
6
Router
w/firewall
Telecommuter
Radius
Server
SSL or IPsec ?

## Slide 147: Intranet VPN
Corporate Network
Branch Network
File servers
CSG
BSG
User
6
5
4
3
2
1

## Slide 148: How Do You Secure Infrastructure ?
Securing Infrastructure Devices
Routing Protocol Security
Securing the Network Perimeter
Securing Remote Access
Mitigating DDoS Attacks

## Slide 149: Today’s DoS Prevention
Allow only good traffic into your network (ingress filtering)
Allow only good traffic out of your network (egress filtering)
Stop directed broadcast traffic (to avoid being an amplifier)
Deny all and permit only what’s needed is most effective policy

## Slide 150: DoS Filtering
Description | Network
default | 0.0.0.0 /8
loopback | 127.0.0.0 /8
RFC 1918 | 10.0.0.0 /8
RFC 1918 | 172.16.0.0 /12
RFC 1918 | 192.168.0.0 /16
Net Test | 192.0.2.0 /24
Testing devices | 192.18.0.0 /15
IPv6 to IPv4 relay | 192.88.99.0 /24
RFC 1918 nameservers | 192.175.48.0 /24
End-node auto configuration | 169.254.0.0 /16

## Slide 151: Reverse Path Forwarding
Ensure input interface is feasible path to source address of incoming packet
Problematic with asymmetric routing

## Slide 152: DoS/DDoS Tools
  Vendor provided
    Arbor TrafGen
  Open source
    stream
    litestorm
    rc8.o
    f__kscript
    slice3

## Slide 153: Audit Tools and Incident Handling
Do you know how to map an IP address to a specific destination?!? (which machine correlates to an IP address)
Ensure timestamps are valid (NTP sources)
Log only what’s needed….avoid information overload

## Slide 154: Data Collection/Correlation
Collecting data
  Time correlation, communications, common formatting, etc.
  These issues are addressed by numerous projects
    IDEF, IDMEF, CIDF, D-Shield, Incidents.org, etc.
Correlating data
  How can we tell what events are related?
  Attacker’s goals determine behavior
  Multiple hypothesis tracking

## Slide 155: Intrusion Detection Systems
Two methods of intrusion detection
  Signature detection (pattern matching)
    Low false positive / Detects only known attacks
  Statistical anomaly detection
    High false positive / Detects wider range of attacks

## Slide 156: Signature vs Anomaly Detection
Modeling signature detection is easy
  If a known attack occurred in an observable area, then p(detection) = 1, else p(detection) = 0
Modeling anomaly detection is more difficult
  Noisy and/or unusual attacks are more likely seen
    Denial of Service, port scans, unused services, etc.
  Other types of attacks may be missed
    Malformed web requests, some buffer overflows, etc.

## Slide 157: Bypassing IDS Systems
How varying TCP/IP stacks behave to slightly invalid input.
  send TCP options, cause timeouts to occur for IP fragments or TCP segments
  overlap fragments/segments
  send slight wrong values in TCP flags or sequence numbers.
  [If overlapping fragments are sent with different data,
  some systems prefer the data from the first fragment
  (WinNT, Solaris), whereas others keep the data from the
  last fragment (Linux, BSD). The NIDS has no way of
  knowing which the end-node will accept, and may guess
  wrong. ]

## Slide 158: IDS Limitations
Vern Paxon’s USENIX presentation in 1998 on ‘Bro - A system for Detecting Network Intruders in real Time’ ftp://ftp.ee.lbl.gov/papers/bro-usenix98-revised.ps.Z
Thomas H. Ptacek and Timothy N. Newsham., "Insertion, Evasion, And Denial Of Service: Eluding Network Intrusion Detection," Technical Report, Secure Networks, Inc., January 1998. http://citeseer.nj.nec.com/ptacek98insertion.html

## Slide 159: Hub vs Switch with IDS
1
2
12
1
2
12
Hub
Switch
Host A
Host B
Host A
Host B
Intrusion
Detection
System
Intrusion
Detection
System
Traffic from host A to host B gets sent to all hub
ports so the IDS can effectively monitor the
traffic.
Traffic from host A to host B gets sent only to
the port which connects host B and the IDS does
not see any traffic.

## Slide 160: Using NIDS with Cable Taps
1
12
2
. . . . . . .
Host A
Host B
Intrusion
Detection
System
Tap
Tap Panel
Tap

## Slide 161: Collecting Incident Data
Traditional Forensics
Immediately shutdown the system (or pull the power cord)
Make a forensic duplicate
Perform analysis on the duplicate
Live system data is rarely recovered.
Infrastructure Forensics
Live system data is the most valuable.
Immediate shutdown destroys all of this data.
Persistent (flash) data will likely be unchanged and useless.
Investigators must recover live data for analysis

## Slide 162: Bare Minimum Device Security
Authenticate and keep track of who has accessed infrastructure devices
Configure access remotely only through ssh or trusted hosts (know what data is sent in the clear)
Disable access that is not used
Accurate timestamps for all logging
Keep keys confidential

## Slide 163: Not To Be Forgotten
DNS Servers
  Lame delegations are evil
  Recursive DNS can lead to cache poisoning
  (UDP – trivial to determine seq# and create invalid entry)
  Block traffic to destination port 53 only and allow traffic to source port 53 that already has an established connection
Email Servers
Spam attacks and deterrents:
http://spam.abuse.net/
http://www.cauce.org/

## Slide 164: What Do I Configure
Device Security
Filtering
Routing Security
IPsec
DoS/DDoS Mitigation
Incident Response

## Slide 165: Generic Device Security Checklist
Console access
Logical access
  telnet vs ssh
  http
  snmp
Logging
Encrypting Passwords

## Slide 166: Device Security Checklist (Layer 3)
Blackhole Filtering
Routing Authentication
ICMP Filters
Other filtering templates

## Slide 167: Device Security Checklist (Layer 2)
MAC Filters
Port Authentication – 802.1x

## Slide 168: What Do I Configure
Device Security
Filtering
Routing Security
IPsec
DoS/DDoS Mitigation
Incident Response

## Slide 169: Making IPsec Configuration Understandable
Vendors have made it hard since no collaboration for defaults (even within same company)
YOU need to define appropriate options

## Slide 170: Pretty Good IPsec Policy
IKE Phase 1 (aka ISAKMP)
  3DES
  Lifetime (how many seconds in 1 day?)
  SHA-1
  DH Group 2 (MODP)
IKE Phase 2 (aka IPsec)
  3DES
  Lifetime (how many seconds in 1 hour?)
  SHA-1
  PFS
  DH Group 2 (MODP)

## Slide 171: PFS- what is it?
Perfect Forward Secrecy
Doing new DH exchange to derive keying material
(DH used to derive shared secret which is used to derive keying material for IPsec security services)

## Slide 172: Advanced Filtering Example
Corporate Campus
Internet
Branch Office A
171.71.77.0
(255.255.255.224)
144.254.0.0
(255.255.255.0)
Branch Office B
192.150.42.0
(255.255.255.224)
Ingress filter from Internet
Egress filter to Internet
Ingress filter from Branch At
Egress filter to Branch A
Ingress filter from Corporate Network
Egress filter to Corporate Network
Ingress filter from Branch B
Egress filter to Branch B
Internet
Ingress filter from Internet
Egress filter to Internet
NOTE BACKDOOR ROUTE TO INTERNET VIA BRANCH B!!

## Slide 173: Branch Router Configuration
The configuration is as follows: (for branch A router)
access-list 133 deny ip host 0.0.0.0 any
access-list 133 deny ip 127.0.0.0 0.255.255.255 any
access-list 133 deny ip 10.0.0.0 0.255.255.255 any
access-list 133 deny ip 172.16.0.0 0.15.255.255 any
access-list 133 deny ip 192.168.0.0 0.0.255.255 any
access-list 133 deny ip 192.0.2.0 0.0.0.255 any
access-list 133 deny ip 169.254.0.0 0.0.255.255 any
access-list 133 deny ip 240.0.0.0 15.255.255.255 any
access-list 133 deny ip 171.71.32.0 0.0.0.31 any
access-list 133 permit ip any any
access-list 144 permit ip 171.71.32.0 0.0.0.31 any
access-list 144 deny ip any any
interface BRI0
description To Corporate Network
ip access-group 133 in
ip access-group 144 out

## Slide 174: NAS Router Policy
Ingress filtering:
permit only traffic with an IP source address of branch networks
deny all other traffic
Egress filtering:
deny all rfc 1918 and special use addresses from propagating
to branch networks
deny all traffic with an IP source address that matches the branch network address allocation
permit all other traffic

## Slide 175: NAS Router Configuration
access-list 133 permit ip 171.71.32.0 0.0.0.31 any
access-list 133 permit ip 192.150.42.0 0.0.0.31 any
access-list 133 deny ip any any
access-list 144 deny ip host 0.0.0.0 any
access-list 144 deny ip 127.0.0.0 0.255.255.255 any
access-list 144 deny ip 10.0.0.0 0.255.255.255 any
access-list 144 deny ip 172.16.0.0 0.15.255.255 any
access-list 144 deny ip 192.168.0.0 0.0.255.255 any
access-list 144 deny ip 192.0.2.0 0.0.0.255 any
access-list 144 deny ip 169.254.0.0 0.0.255.255 any
access-list 144 deny ip 240.0.0.0 15.255.255.255 any
access-list 144 deny ip 171.71.32.0 0.0.0.31 any
access-list 144 deny ip 192.150.42.0 0.0.0.31 any
access-list 144 permit ip any any
interface Serial 0:23
description To Branch Offices
ip access-group 133 in
ip access-group 144 out

## Slide 176: Internet Router Policy
Ingress filtering:
deny all rfc 1918 and special use addresses
from entering the corporate network
deny all traffic with an IP source address of the corporate
network or branch networks
permit all other traffic
Egress filtering:
permit only traffic with an IP source address of the
corporate network and branch networks
deny all other traffic

## Slide 177: Internet Router Configuration
access-list 133 deny ip host 0.0.0.0 any
access-list 133 deny ip 127.0.0.0 0.255.255.255 any
access-list 133 deny ip 10.0.0.0 0.255.255.255 any
access-list 133 deny ip 172.16.0.0 0.15.255.255 any
access-list 133 deny ip 192.168.0.0 0.0.255.255 any
access-list 133 deny ip 192.0.2.0 0.0.0.255 any
access-list 133 deny ip 169.254.0.0 0.0.255.255 any
access-list 133 deny ip 240.0.0.0 15.255.255.255 any
access-list 133 deny ip 144.254.0.0 0.0.255.255 any
access-list 133 deny ip 171.71.32.0 0.0.0.31 any
access-list 133 deny ip 192.150.42.0 0.0.0.31 any
access-list 133 permit ip any any
access-list 144 permit ip 144.254.0.0 0.0.255.255 any
access-list 144 permit ip 171.71.32.0 0.0.0.31 any
access-list 144 permit ip 192.150.42.0 0.0.0.31 any
access-list 144 deny ip any any
interface Serial 0/0
description To Internet
ip access-group 133 in
ip access-group 144 out

## Slide 178: Session Summary
Create a usable security policy
Limit access to infrastructure devices
Provide good levels of authentication (ssh, one-time-password)
FILTER at the EDGE
Use route authentication
Audit your network infrastructures

## Slide 179: Configuring IPsec
STEP 1 Configure the IKE Phase 1 Policy (ISAKMP Policy)
Cisco literature refers to IKE Phase 1 as the ISAKMP policy.
It is configured using the command:
crypto isakmp policy priority
Multiple policies can be configured and the priority number, which ranges
from 1 to 10,000, denotes the order of preference that a given policy will be
negotiated with an ISAKMP peer. The lower value has the higher priority.
Once in the ISAKMP configuration mode, the following parameters can be
specified are:
Encryption Algorithm
Hash Algorithm
Authentication Method
Group Lifetime

## Slide 180: Configuring IPsec
STEP 2 Set the ISAKMP Identity
The ISAKMP identity specifies how the IKE Phase 1 peer is identified,
which can be either by IP address or host name.
The command to use is:
crypto isakmp identity {IP address | hostname}
By default, a peer’s ISAKMP identity is the peer’s IP address.
If you decide to change the default just keep in mind that it is
best to always be consistent across your entire IPsec-protected
network in the way you choose to define a peer’s identity.

## Slide 181: Configuring IPsec
STEP 3 Configure the IPsec AH and ESP Parameters
The AH and ESP parameters are configured with the following commands:
crypto ipsec transform-set transform-set-name <transform 1> <transform 2>
mode [tunnel | transport]
crypto ipsec security-association lifetime seconds seconds

## Slide 182: Configuring IPsec
STEP 4 Configure the IPsec Traffic Selectors
The traffic selectors are configured by defining extended access-lists.
The permit keyword causes all IP traffic that matches the specified
conditions to be protected by IPsec
STEP 5 Configure the IKE Phase 2 (IPsec SA) Policy
This step sets up a crypto map which specifies all the necessary
parameters to negotiate the IPsec SA policy. The following commands are required:
crypto map crypto-map-name seq-num ipsec-isakmp
match address access-list-id
set peer [IP address | hostname]
set transform-set transform-set-name
set security-association lifetime seconds seconds
set pfs [group1 | group 2]

## Slide 183: Configuring IPsec
STEP 6 Apply the IPsec Policy to an Interface
The configured crypto map is then applied to the appropriate
interface using the crypto map crypto-map-name command.
It is possible to apply the same crypto map to multiple interfaces.
This case would require the use of the command:
crypto map crypto-map-name local-address interface-id
Using this command, the identifying interface will be used as the local address
for IPsec traffic originating from or destined to those
interfaces sharing the same crypto map. A loopback interface should
be used as the identifying interface.

## Slide 184: Additional IPsec Considerations
What happens when dynamic IP addresses are used?
How do you authenticate the actual user as well as the device?

## Slide 185: Detecting An Incident
Accounting discrepancies
Data modification and deletion
Users complaining of poor system performance
Atypical traffic patterns
Atypical time of system use
Large numbers of failed login attempts

## Slide 186: Incident Response
DO NOT REBOOT THE DEVICE.
Change nothing, record everything.
Before you say it is an accident, make sure it isn’t an incident…
Before you say it is an incident, make sure it isn’t an accident…

## Slide 187: Incident Response Evidence
Detailed, Methodical, Unquestionable….
Where you received the evidence…
When you received the evidence…
Who you received the evidence from…
What your seizure methods were…
Why you seized the evidence…
How you maintained your chain of custody…

## Slide 188: Assessing Damage
Check log statistics for unusual activity on corporate perimeter network access points, such as Internet access or dial-in access.
Verify infrastructure device checksum or operating system checksum on critical servers to see whether operating system software has been compromised.
Verify configuration changes on infrastructure devices and servers to ensure that no one has tampered with them.
Check sensitive data to see whether it was accessed or changed.
Check traffic logs for unusually large traffic streams from a single source or streams going to a single destination.
Run a check on the network for any new or unknown devices.
Check passwords on critical systems to ensure that they have not been modified (it would be prudent to change them at this point).

## Slide 189: Reporting Guidelines
Keep the technical level of detail low.
Work with law enforcement officials to ensure that evidence is protected.
Delegate all handling of the public to in-house PR people who know how to handle the press.
Do not break or halt lines of communication with the public.
Keep the speculation out of public statements.
Do not allow the public attention to detract from the handling of the event.

## Slide 190: RFC 3013 (Recommended ISP Security Services & Procedures)
ISPs have a duty to make sure that their contact information, in Whois, in routing registries [RFC1786] or in any other repository, is complete, accurate and reachable.
ISPs should have processes in place to deal with security incidents that traverse the boundaries between them and other ISPs.
ISPs SHOULD be able to conduct such communication over a secure channel.
ISPs SHOULD be proactive in notifying customers of security vulnerabilities in the services they provide.

## Slide 191: RFC 3013 Notifying Customers
  who is coordinating response to the incident
  the vulnerability
  how service was affected
  what is being done to respond to the incident
  whether customer data may have been compromised
  what is being done to eliminate the vulnerability
  the expected schedule for response, assuming it can be predicted
Information that should be included:

## Slide 192: THANK YOU!
From:
Designing Network Security, 2nd Edition
ISBN 1587051176
http://www.ciscopress.com/title/1587051176
By Merike Kaeo.
Published by Cisco Press.
Series: Networking Technology